## Slide 1: Relaxed Consistency Part 2
David Devecsery

## Slide 2: Administration!
  Syllabus quiz error!
    Was labeled as due Aug 22nd. Your submission will not be counted as late
    Still Due Sep. 4th.
  Reading for next class
    2 Reviews
  Discussion sign-ups
    Start thinking about what topics you’ll want to lead the discussion for.

## Slide 3: Can this dereference null?
Out-of-order
Memory
Load Buffer
ready, a
Store Queue
Out-of-order
Load Buffer
Store Queue
a, ready
Processor 1
a = new int[10];
ready = true;
Processor 2
if (ready)
a[5] = 5;
Initial: ready = false, a = null
Processor 1
Processor 2
Problem:
Our out-of-order loads are speculating that data won’t be changed by processor 1
a = null
Notes: ANIMATIONS

## Slide 4: Can this dereference null?
Out-of-order
Load Buffer
  Goal: Identify when our speculation (load data isn’t changed by another processor) is incorrect.
Memory
a
ready
a = null
null
Out-of-order
Store Queue
a
ready
a = new…
Can we now release a’s value?
Idea:
Have memory notify the load buffer when a value changes
new…
true
Hold loads until all dependent (by program order) loads are done
ready = true
a = new…
ready = true
true
new…
Memory alerts load buffer of change to “a”
Notes: ANIMATIONS

## Slide 5: Intro cache consistency
Explain MSI cache coherency
  First do the caches on a shared bus
  Then talk about the states, Modified, Shared, Invalid
  Then give operations (read, write, invalidate)
    FSM
  Then, talk about how to integrate this to handle loads

## Slide 6: Introduction to Memory Models
Partial Consistency (PC) [x86]
Stores to the same location by a single processor
core are ordered
Every store in a thread to a variable happens before the next store in that thread to that variable

## Slide 7: Introduction to Memory Models
Can this code have a null pointer exception under PC?
Thread 1
a = new int[10];
Thread 2
while (a == null);
ready1 = true;
Initial: a = null, ready = false
Thread 3
while (ready1 == false) ;
print a[0];
Remember, ordering is based off each location
Answer: Yes

## Slide 8: Introduction to Memory Models
Can this code have a null pointer exception under PC?
Thread 1
a = new int[10];
Thread 2
while (a == null);
ready1 = true;
Initial: a = null, ready = false
Thread 3
while (ready1 == false) ;
print a[0];
Remember, ordering is based off each location

## Slide 9: Introduction to Memory Models
Can this segfault under PC?
Thread 1
a = new int[10];
ready = true;
Thread 2
if (ready)
a[5] = 5;
Initial: ready = false, a = null
Answer: Absolutely!

## Slide 10: Memory systems for: Partial Consistency
Out-of-order (memory subsystem)
Memory
Load Buffer
Store Queue
Loads run in parallel, integrate with memory to guarantee store order is observed
Stores are queued, and execute in FIFO order
How can we create a partially consistent system?
Stores can run in parallel, as long as other stores to the same address on this core have run
Loads run in parallel

## Slide 11: Can this segfault?
Out-of-order
Memory
Load Buffer
Parallel Store Queue
Out-of-order
Load Buffer
Parallel Store Queue
Processor 1
Processor 2
Thread 1
a = new int[10];
ready = true;
Thread 2
if (ready)
a[5] = 5;
Initial: ready = false, a = null
Notes: ANIMATIONS

## Slide 12: Partial consistency: locking
Will this code enforce mutual exclusion on a PC MM?
Lock:
do {
tmp = xchg(unlocked, 1);
if (tmp != 1) {
while (unlocked != 1) ;
}
} while (tmp != 1)
Unlock
unlocked = 1
xchg (x, y):
atomic {
old = x;
x = y;
return old
}
Hint: Think of using the synchronization to lock another variable:
lock()
y = 1
unlock ()

## Slide 13: Partial consistency: locking
Question: How do I build a lock on a partially consistent system?
Answer: I need a way to stop load and store reordering!
Provided via Fences (also called memory barriers)

## Slide 14: Relaxed consistency: barriers
X86 [X]Fences: All X instructions before the fence will be globally visible to all X instructions following the fence
MFENCE (load or store) – Handout provided
SFENCE (stores only) – Handout provided
LFENCE (loads only) – Handout provided
NOTE: x86 also has a LOCK prefix, it is needed and related to fences, but different

## Slide 15: Partial consistency: barriers
Can we use fences to make this mutually exclusive?
Lock:
do {
tmp = xchg(unlocked, 0);
if (tmp != 1) {
while (unlocked != 1) ;
}
} while (tmp != 1)
Unlock
unlocked = 1
xchg (x, y):
atomic {
old = x;
x = y;
return old
}

## Slide 16: Introduction to Memory Models
What can this code print, under TSO?
Thread 1
a = 1
MFENCE
print b
Thread 2
b = 1
MFENCE
print a
Initial: a = 0, b = 0

## Slide 17: Can this segfault?
Out-of-order
Memory
Load Buffer
Parallel Store Queue
Out-of-order
Load Buffer
Parallel Store Queue
Processor 1
Processor 2
Thread 1
a = 1
MFENCE
print b
Thread 2
b = 1
MFENCE
print a
Initial: a = 0, b = 0
Notes: ANIMATIONS

## Slide 18: Introduction to Memory Models
What can this code print, under TSO?
Thread 1
a = 1
LFENCE
print b
Thread 2
b = 1
LFENCE
print a
Initial: a = 0, b = 0

## Slide 19: Introduction to Memory Models
What can this code print, under TSO?
Thread 1
a = 1
SFENCE
print b
Thread 2
b = 1
SFENCE
print a
Initial: a = 0, b = 0

## Slide 20: Brand new architecture!
Read question 5, Billy-Jean’s architecture.

## Slide 21: In what ways can we reorder operations?
  Data Reordering
    Read-read
    Read-write
    Write-write
  Memory Atomicity
    When a store goes to memory, is it visible to all processors?

## Slide 22: Reorderings happen at two layers
  Within the core
  Within the memory
Out-of-order
Memory
Load Buffer
Parallel Store Queue
Out-of-order
Load Buffer
Parallel Store Queue
Processor 1
Processor 2

## Slide 23: How do we handle these reorderings?
  Introduction of barriers
    Stop reordering of certain instructions around barriers
  Can programmers really be expected to reason about barriers and instruction reorderings throughout their programs?

## Slide 24: “Weak Ordering – A New Definition” Adve and Hill
  “[…] a description of memory should not require the specification of the performance enhancing features of the underlying hardware. Rather, such features should be camouflaged by defining the memory model in terms of constraints on software which, if obeyed, make the weaker system appear sequentially consistent.”
  Idea: There should be a contract between the program and the hardware, if that contract is met, the program runs as SC

## Slide 25: DRF-0
  Idea: If we can impose a happens-before order between two memory accesses on a weakly ordered processor, then the accesses appear sequentially consistent.
  Happens before orderings:
    Program Order: Order of program operations on a single core
    Synchronization Order: Order of synchronizations (special operations synchronizing a memory location between two cores)

## Slide 26: Ordering example
  These operations all have well defined orderings:
  ex. W(y, P1) S(a, P1) S(a, P2) R(y, P2)
      W(y, P1) R(y, P1)
W(x)
P0
P1
P2
P3
P4
P5
R(x)
W(y)
S(a)
S(a)
R(y)
W(z)
S(b)
S(b)
S(c)
R(z)
PO
PO
PO
PO
PO
SO
SO
SO

## Slide 27: Are these accesses ordered?
Which of the above accesses are unordered?
W(x)
P0
P1
P2
P3
P4
P5
R(x)
W(y)
S(b)
S(b)
PO
PO
PO
SO
R(x)
R(z)
W(z)
S(c)
S(c)
SO
PO
SO
R(z)
S(d)
PO
PO
S(d)
PO
What’s the defined behavior between these unordered operations?

## Slide 28: Trade-offs of DRF-0
  What are the advantages and disadvantages of DRF0?
  Advantages
  Disadvantages

## Slide 29: “Weak Ordering- A New Definition”
  What do you believe the advantages of this approach are?

## Slide 30: Next Class
  When do these high-level abstractions break down
    What does that look like?
    How should we solve it?